## Slide 1
Recuperated solar-dish Brayton cycle with turbocharger and short-term thermal storage
Department of Mechanical and Aeronautical Engineering,
University of Pretoria
Dr WG Le Roux

## Slide 2: Background
2
Long-term average of direct normal solar irradiance on a world map showing the potential of solar power generation in southern Africa (GeoModel Solar, 2014)

## Slide 3: Background
3
South Africa has one of the best solar resources in the world and this resource is free to use and study for all South Africans, who should take the lead in this field in terms of
  skills development,
  training and
  product manufacturing.
The research and development of solar dish technologies is a new and exciting research field in which all South African researchers of all age, race and gender can take the lead.

## Slide 4: Background
4
Power generation
Water purification
Fuel production

## Slide 5: Presentation Outline
5
Introduction and Background
Problem and Purpose
Methodology
Results and Discussion
Conclusion
Progress to date (Solar@UP)
  Solar radiation in Pta
  New dish concept
  Moonlight testing
  Receiver testing
  Recuperator testing

## Slide 6: 1. Introduction
6
Solar-Dish Brayton Cycle
small-scale
dish-mounted
with recuperator
1-20kW
turbocharger
open-cavity tubular receiver
Air in
10
Air out
3
4
7
8
9
11
5
2
6
1
Proposed turbocharger to use as micro-turbine
(Image extracted from Garrett, 2014)

## Slide 7: 1. Introduction
7
The small-scale dish-mounted solar thermal Brayton cycle with recuperator (STBC)

## Slide 8: 1. Introduction
8
Solar thermal Brayton cycle
advantages
Air as working fluid
Turbocharger as micro-turbine
Can also be powered with gas (hybrid system)
Water heating (cogeneration)
High efficiency potential (reheat and intercooling)
Mobility
Cost benefits (bulk manufacturing)
Thermal storage
Quicker to commercialise (prototyping is quicker and cheaper)
Large-scale local manufacturing – good for the economy (good for South Africa)
Micro-grids
Air in
10
Air out
3
4
7
8
9
11
5
2
6
1

## Slide 9: 1. Introduction
9
Solar thermal Brayton cycle advantages
Recuperator
  allows for higher efficiency at lower compressor pressure ratios
  allows for a less complex receiver (operating at lower pressure and smaller temperature increase)
Image extracted from: Stine, B.S., Harrigan, R.W., 1985, Solar energy fundamentals and design. New York: John Wiley & Sons, Inc.

## Slide 10: 1. Introduction
10
Solar thermal Brayton cycle advantages
Turbocharger
  The maximum inlet temperature of an off-the-shelf turbocharger is about 1223 K (Garrett, 2014; Shah, 2005) and 1323 K intermittently.
Proposed turbocharger to use as micro-turbine
(Image extracted from Garrett, 2014)

## Slide 11: 1. Introduction
11
Turbocharger
  Generator coupling
Generator coupling – simple, robust, easy to maintain
(Image extracted from Shiraishi and Ono, 2007)
Range extenders in electric vehicles

## Slide 12: 1. Introduction
12
Turbocharger
  Generator coupling
Generator coupling – simpe, robust, easy to maintain
(Image extracted from Shiraishi and Ono, 2007)

## Slide 13: 1. Introduction – Open cavity tubular receiver
13
Receiver dimensions optimised in a previous work (Le Roux et al., 2014)

## Slide 14: 1. Introduction – Open cavity tubular receiver
14
Heat up insulated receiver to 857 °C
  using 86 kW LPG flame from Sievert burner
Inlet
Outlet

## Slide 15: 1. Introduction – Brayton cycle thermal storage
15

## Slide 16: 1. Introduction – Brayton cycle thermal storage
16

## Slide 17: 1. Introduction
17
Thermal storage
  Lithium fluoride (Cameron et al., 1972; Asselman, 1976)
  Packed rock beds (Allen, 2010; Ozturk et al., 2019),
  Encapsulated sodium sulphate (Klein, 2016)
  Phase-change materials can be used to provide a stable turbine inlet temperature;
    however, most phase-change materials have a low thermal conductivity of around 0.5 W/mK (Liu et al., 2012).
    metallic phase-change materials have higher thermal conductivities.
    Other materials such as salt composites and inorganic salts have limited applications because of large volume changes during melting as well as corrosion issues (Liu et al., 2012).

## Slide 18: 1. Introduction (Solar-dish Brayton cycle) – Metallic phase-change materials (Liu et al. 2012)
18
Phase-change material | Composition (wt%) | Melting temperature (K) | ρ (kg/m3) | cp,solid (J/kgK) | cp,liquid (J/kgK) | k (W/mK) | Latent heat, Lf (kJ/kg)
Mg |  | 921 | 1740 | 1270 | 1370 |  | 365
Al |  | 933 | 2700 | 900 | 1100 | 186 | 397
Zn–Cu–Mg | 49/45/6 | 976 | 8670 | 420 |  |  | 176
Cu–P | 91/9 | 988 | 5600 |  |  |  | 134
Cu–Zn–P | 69/17/14 | 993 | 7000 |  |  |  | 368
Cu–Zn–Si | 74/19/7 | 1038 | 7170 |  |  |  | 125
Cu–Si–Mg | 56/27/17 | 1043 | 4150 | 750 |  |  | 420
Mg–Ca | 84/16 | 1063 | 1380 |  |  |  | 272
Mg–Si–Zn | 47/38/15 | 1073 |  |  |  |  | 314
Cu–Si | 80/20 | 1076 | 6600 | 500 |  |  | 197
Cu–P–Si | 83/10/7 | 1113 | 6880 |  |  |  | 92
Si–Mg–Ca | 49/30/21 | 1138 | 2250 |  |  |  | 305
Si-Mg | 56/44 | 1219 | 1900 | 790 |  | 70 | 757

## Slide 19: 2. Problem and Purpose
19
Problem
  the phase-change temperature affects the solar conversion efficiency
Purpose of the study
Determine maximum thermal efficiency of the cycle for
  an off-the-shelf turbochargers
  various recuperator geometries
  fixed receiver geometry
  Metallic phase-change material at different solar receiver temperatures

## Slide 20: 3. Methodology - Receiver
20
Assumptions for receiver:
Constant surface temperature tube, at steady state (Ts = PCM temperature
Koenig and Marvin heat loss model for cavity receiver

## Slide 21: 3. Methodology - Recuperator
21
Assumptions for recuperator:
Effectiveness-NTU model including heat loss to the environment (Nellis and Pfotenhauer, 2005)

## Slide 22: 3. Methodology - Turbocharger
22
Assumptions for turbocharger:
Determine mass flow rate and pressure ratios from the compressor map and turbine map (GT2052)

## Slide 23: 3. Methodology - Turbocharger
23
Assumptions for turbocharger:
Determine mass flow rate and pressure ratios from the compressor map and turbine map

## Slide 24: 3. Methodology – Parameters
24
Power output calculation:
The MATLAB program has the following stucture:
For Ts = 900:100:1200,
For each turbine pressure ratio (rt) in the operating range of the turbine,
For each recuperator design (625 different combinations),
Find net power output and efficiency
of cycle.

## Slide 25: 3. Methodology – Net power output
25
Entropy generation minimisation to optimise geometries of components for a common goal

## Slide 26: 4. Results and discussion- thermal efficiency
26
Maximum thermal efficiency of the cycle for different turbine pressure ratios and receiver tube surface temperatures (for GT2052).
Maximum thermal efficiencies of 20.2% to 34.2%

## Slide 27: 4. Results and discussion – receiver heat loss
27
Heat loss rate from the solar receiver as a function of tube surface temperature.

## Slide 28: 4. Results and discussion – performance map
28
Net power output at maximum thermal efficiency for GT2052 as a function of dish size

## Slide 29: 4. Results and discussion – solar conversion efficiency
29
Maximum solar conversion efficiency for GT2052.
Maximum solar conversion efficiencies of 13.5% to 21% can be achieved at receiver temperatures of between 900 K and 1200 K.

## Slide 30: 4. Results and discussion
30
Temperature in the cycle at different receiver surface temperatures for maximum thermal efficiency (for GT2052).

## Slide 31: 4. Results and discussion
31
Pressure in the cycle at different receiver surface temperatures for maximum thermal efficiency (for GT2052).

## Slide 32: 4. Results and discussion – storage time
32
Thermal storage time available at the phase-change temperature.
For VPCM = 0.05 m3

## Slide 33: 4. Results and discussion – storage time
33
For VPCM = 0.05 m3
Molten aluminum in the receiver at 933 K, could be worth investigating further as a simple and low-cost solar-dish Brayton cycle configuration.

## Slide 34: 5. Conclusion
34
Solar-dish Brayton cycle advantages:
  air as working fluid
  cogeneration
  hybridisation
  thermal storage
  cost benefits, benefits for the economy
Problem - the phase-change temperature affects the solar conversion efficiency
Purpose
  Determine maximum thermal efficiency of the cycle for
    off-the-shelf turbocharger
    various recuperator geometries
    fixed receiver geometry
    metallic phase-change material at different solar receiver temperatures

## Slide 35: 5. Conclusion
35
Maximum thermal efficiencies of 20.2% to 34.2%
Maximum solar conversion efficiencies of 13.5% to 21% can be achieved at receiver temperatures of between 900 K and 1200 K.
Overall, the results show that an open-cavity tubular solar receiver with metallic phase-change thermal storage material can be used together with an off-the-shelf turbocharger for power generation in a recuperated solar-dish Brayton cycle.
The GT2052 operating with molten aluminium in the receiver is recommended for further analytical and experimental investigation.

## Slide 36
Solar@UP
Department of Mechanical and Aeronautical Engineering,
University of Pretoria
Dr WG Le Roux
TIA funded project:
Building a prototype:
Recuperated solar-dish Brayton cycle with turbocharger

## Slide 37
Solar @ UP – Very good DNI (SAURAN)

## Slide 38
Solar @ UP – old dish

## Slide 39
Solar @ UP – old dish

## Slide 40
Solar @ UP – old dish

## Slide 41
Solar @ UP – Solar receiver testing

## Slide 42
Solar @ UP – CFD (Prof. Ken Craig)

## Slide 43
Solar @ UP – new dish

## Slide 44
Solar @ UP – new dish

## Slide 45
Solar @ UP – new dish

## Slide 46
Solar @ UP - new dish

## Slide 47
Solar @ UP – new dish

## Slide 48
Solar @ UP – new dish (photogrammetry)

## Slide 49
Solar @ UP – New dish (Moonlight testing)

## Slide 50
Solar @ UP – New dish (Moonlight testing)

## Slide 51
Solar @ UP

## Slide 52
Solar @ UP – New dish (Moonlight testing)

## Slide 53
Solar @ UP – New dish (Moonlight testing)

## Slide 54
Solar @ UP – New dish (Moonlight testing)

## Slide 55
Solar @ UP – Smaller dish setup (moonlight testing)

## Slide 56
Solar @ UP – Smaller dish setup (moonlight testing)

## Slide 57
Solar @ UP – Smaller dish setup (moonlight testing)

## Slide 58
Solar @ UP – Smaller dish setup (moonlight testing)

## Slide 59
Solar @ UP
– Moonlight testing for flux mapping

## Slide 60
Solar @ UP
– Moonlight testing for flux mapping

## Slide 61
Solar @ UP – Recuperator testing

## Slide 62: Acknowledgements
62
This work is based on the research supported by the
  Technology Innovation Agency (TIA),
  National Research Foundation (NRF),
  Royal Society, UK,
SAURAN is acknowledged for the data used (temperature and wind measurements)

## Slide 63: Thank you
63
Questions?
willem.leroux@up.ac.za